## Slide 1: What’s new in fireware 12.10.3

## Slide 2: What’s new in Fireware v12.10.3
Log Message Updates for ThreatSync+ NDR
Resolved Issues

## Slide 3: What’s new in Fireware v12.10.3
Fireware v12.10.3 is available for these Firebox models:
  Firebox M Series: M270, M290, M370, M390, M440, M470, M570, M590, M670, M690, M4600, M4800, M5600, M5800
  Firebox T Series: T20, T25, T40, T45, T55, T70, T80, T85
  Firebox NV5
  FireboxV and Firebox Cloud
Fireware v12.10.3 does not support these models:
  Firebox T15 and Firebox T35
  We continue to support these models with Fireware v12.5.x firmware. For more information, see this KB article

## Slide 4: Log Message Updates for ThreatSync+ NDR

## Slide 5: Log Message Updates for ThreatSync+ NDR
Fireware v12.10.3 includes log message updates to support a future ThreatSync+ NDR release
In Fireware v12.10.3 and higher, some types of log messages now include this information:
  duration – Duration of the connection
  sent_pkts – Packets sent
  rcvd_pkts – Packets received
  type – For ICMP connections, the ICMP type number

## Slide 6: Log Message Updates for ThreatSync+ NDR
Information added to some log messages for ThreatSync+ NDR (cont):
  flags – Flags that provide additional information about the connection. Flags vary by log message type and protocol:
    TCP traffic flags:
      S – New (not established) with no response (timeout)
      SR – New (not established) with negative response RST, or a new connection (not established) and denied by firewall policies
      SDdF – Established and normal termination by FIN
      SD – Established with timeout or terminated by RST, or an established connection denied by a security service, such as Intrusion Prevention Service (IPS)
    UDP traffic flags:
      D – New with no response (traffic from only one direction) and timeout
      Dd – Established (traffic from both directions) and normal termination

## Slide 7: Log Message Updates for ThreatSync+ NDR
Proxy-related log messages only include the new information when the Firebox is allocated to a WatchGuard Cloud account with ThreatSync+ NDR
For more information on log messages generated by the Firebox, go to the Fireware Log Catalog

## Slide 8: Resolved Issues

## Slide 9: Resolved Issues
Fireware v12.10.3 is a maintenance release that includes important resolved issues
For detailed information about the issues resolved in this release, see the Release Notes:
  Fireware v12.10.3 Release Notes