## Slide 1: What’s new in fireware 12.12.1

## Slide 2: What’s new in Fireware v12.12.1
Encrypt the Firebox Configuration File
USB Backup Image and Auto-Restore Updates

## Slide 3: What’s new in Fireware v12.12.1
Fireware v12.12.1 is available for these Firebox models:
  Firebox M270, M290, M370, M390, M470, M570, M590, M670, M690, M4600, M4800, M5600, M5800
  Firebox T20, T25, T40, T45, T80, T85
  Firebox NV5
  FireboxV and Firebox Cloud
Fireware v12.12.1 does not support these models:
  Firebox T115, T125, T145, T185, M295, M395, M495, M595, M695 (v2026.x firmware)
  Firebox T15 and Firebox T35 (v12.5.x firmware)
For more information on supported Firebox models, go to this KB article

## Slide 4: Encrypt the Firebox Configuration File

## Slide 5: Encrypt the Firebox Configuration File
You can now specify a password to encrypt the Firebox configuration file when you download it from Fireware Web UI
You use this password to unzip the downloaded .ZIP file that contains the configuration file
For more information, go to Manage the Firebox Configuration File in Help Center

## Slide 6: Encrypt the Firebox Configuration File
To download and encrypt the configuration file, from Fireware Web UI:
  Select System > Configuration File
  Click Download the Configuration File
  Type and confirm a password to use to encrypt the configuration file
  Click Save
  Select the location where you want to save the exported configuration file

## Slide 7: USB Backup Image and Auto-Restore Updates

## Slide 8: USB Backup Image and Auto-Restore Updates
USB backup images no longer include the Fireware OS, and the "Include OS" option has been removed from USB backup in the Fireware Web UI.
USB restore via the Fireware Web UI and Setup Wizard now performs a configuration-only restore. If you restore an older backup image that includes an embedded OS, the OS is ignored and only the configuration is restored.
USB backup image restores now require that the Fireware OS version and build of the backup image match the version and build installed on the Firebox
  If they do not match, the restore is blocked
  To restore the backup image, first upgrade or downgrade the Firebox to the matching Fireware version and build

## Slide 9: USB Backup Image and Auto-Restore Updates
USB Auto-Restore Backup Image changes after upgrade:
  To be able to restore a new USB auto-restore backup image created in v12.12.1 and higher, you must first upgrade the recovery partition (sysB) of the Firebox
  For instructions on how to download and install the software update for the recovery partition (sysB), go to this WatchGuard Knowledge Base article

## Slide 10: USB Backup Image and Auto-Restore Updates
  You can no longer select to include the Fireware OS in the backup image as in previous Fireware versions
  You must manually place the Fireware OS image file, [Firebox_model_version].sysa-dl, in the same USB \auto-restore folder as the auto-restore.fxi file For example: \auto-restore\[Firebox_model]\ auto-restore.fxi [Firebox_model_version].sysa-dl auto-restore-info.txt
  After you upgrade the Firebox recovery partition (sysB), backup images created on both previous Fireware versions and v12.12.1 and higher must have the matching Fireware OS image manually placed in the \auto-restore folder

## Slide 11: USB Backup Image and Auto-Restore Updates
If you have not yet upgraded your recovery partition (sysB), USB auto-restore backup images created with previous Fireware versions will continue to work for auto-restore
After you upgrade the recovery partition (sysB), USB auto-restore backup images created with previous Fireware versions will continue to work for auto-restore, but you must:
  Manually place the matching Fireware OS .sysa-dl file in the \auto-restore folder on the USB drive. Any embedded OS in the backup image is ignored.
  Root CA certificates from the previous Fireware version backup image are not restored. The Firebox boots with default certificates for the installed firmware version. You must manually re-import any certificates you imported previously.

## Slide 12: USB Backup Image and Auto-Restore Updates
For more information, go to these topics in Help Center:
  Use a USB Drive for System Back and Restore
  Automatically Restore a Backup Image from a USB Drive

## Slide 13: Thank you