## Slide 1: What’s New in Fireware v12.5.6/12.6.3

## Slide 2: What’s New in Fireware v12.5.6/12.6.3
Dynamic routing — default route announcements
Flood protection logging update
New Mobile VPN with SSL Client (v12.6.3 only)
Resolved issues

## Slide 3: What’s New in Fireware v12.5.6/12.6.3
Fireware v12.6.3 is available for these Firebox models:
  M Series: M270, M370, M400, M440, M470, M500, M570, M670, M4600, M5600
  T Series: T20, T40, T80
  FireboxV and Firebox Cloud
Fireware v12.5.6 runs on all other Firebox models
Unless noted, the features described in this document are available in both Fireware v12.5.6 and Fireware v12.6.3

## Slide 4: What’s New in Fireware v12.5.6/12.6.3
Use WSM v12.6.3 to manage Fireboxes that run Fireware v12.5.6 or Fireware v12.6.3
There is no WSM v12.5.6

## Slide 5: Dynamic Routing — Default Route Announcements

## Slide 6: Dynamic Routing — Route Announcements
For a Firebox with an IPv4 dynamic routing configuration that includes the command default-information originate (in OSPF or RIP) or default-originate (in BGP), if Link Monitor detects a link failure for all WAN connections, the dynamic routing protocol no longer announces the default route to neighbors

## Slide 7: Flood Protection Logging Update

## Slide 8: Flood Protection Logging Update
The Firebox now generates log messages when traffic from a site on the Blocked Site Exceptions list exceeds a Flood Attack threshold
  Example:
  Dec 16 19:14:00 2020 M370 local0.warn firewall: msg_id="3000-0148" Allow eth4 Firebox 28 icmp 20 64 10.0.0.1 10.0.0.3 8 0 id=54614 seq=16296 msg="icmp flooding from exception site" (Internal Policy)
As in previous Fireware versions, the Firebox allows the traffic

## Slide 9: New Mobile VPN with SSL Client (v12.6.3 Only)

## Slide 10: Mobile VPN with SSL Client (v12.6.3 Only)
Fireware v12.6.3 includes a new version of the Mobile VPN with SSL Client for Windows and macOS
This version resolves a number of Mobile VPN issues
  Note: Both v12.5.3 and v12.6.3 of the Mobile VPN with SSL Client are compatible with both Fireware v12.5.6 and Fireware v12.6.3 on supported versions of Windows and macOS

## Slide 11: Resolved Issues

## Slide 12: Resolved Issues
Fireware v12.5.6/v12.6.3 are maintenance releases that include important resolved issues
For detailed information about the issues resolved in these releases, see the Release Notes:
  Fireware v12.5.6 Release Notes
  Fireware v12.6.3 Release Notes

## Slide 13: Thank You!