## Slide 1: What’s new in fireware 12.8

## Slide 2: What’s new in Fireware v12.8
SD-WAN Round Robin
SD-WAN Actions in Centralized Management
External VLAN Enhancements
Set External Interface and VLAN ID in Quick Setup Wizard
MOBIKE Support for Mobile VPN with IKEv2
Intra-Interface Inspection
IPv6 in Bridge Mode
Disable GARP
Disable the Geolocation Deny Page
Specify Logging and Notification Settings for Default Packet Handling

## Slide 3: What’s new in Fireware v12.8
APT Blocker Automatically Submits PDF Files for Analysis
DF Bit for Mobile VPN with IKEv2
System Integrity Checks
Firebox Management Policy Warnings
OS checksum

## Slide 4: What’s new in Fireware v12.8
Fireware v12.8 is available for these Firebox models:
  Firebox M Series: M270, M290, M370, M390, M400, M440, M470, M500, M570, M590, M670, M690, M4600, M4800, M5600, M5800
  Firebox T Series: T20, T40, T55, T70, T80
  FireboxV and Firebox Cloud
Fireware v12.8 does not support these models:
  Firebox T10, T15, T30, T35, T50, M200, M300
  We continue to support these models with Fireware v12.5.x firmware. For more information, see this KB article

## Slide 5: SD-WAN ROUND ROBIN

## Slide 6: SD-WAN Round Robin
You can now configure an SD-WAN action to use the Round Robin method
  Round Robin is a load-balancing method that distributes outgoing traffic between multiple interfaces based on weight and other factors
You can use SD-WAN Round Robin to:
  Share traffic load across multiple ISPs or lines
  Get the full benefit from all ISP connections to which your company subscribes. For example, you can use a secondary connection for more than just redundancy

## Slide 7: SD-WAN Round Robin
For traffic that matches the SD-WAN action, the Firebox considers these factors to determine the outgoing interface:
  Weight — A number that you assign to each interface in an SD-WAN action. Weight corresponds to the proportion of traffic load that the Firebox sends through an interface. A higher number indicates a greater load.
  3-tuple — Source IP address, destination IP address, and protocol for packets handled by an SD-WAN action. Connections are sticky, which means traffic from the same source to the same destination using the same protocol is always routed through the same interface.
  Measures (Optional) —Loss rate, latency, and jitter for each interface in an SD-WAN action

## Slide 8: SD-WAN Round Robin
Example
  You have two WAN links of unequal capacity for redundancy. To take advantage of the redundant link, you want to distribute outbound Internet traffic over both links.
  Configure an SD-WAN action that includes the two WAN interfaces, External-1 and External-2. The External-1 link has more capacity.
    In the SD-WAN action, assign a weight of 6 to the External-1 interface and a weight of 4 to the External-2 interface
    If 10 connections match the SD-WAN action, the External-1 interface handles 6 of those connections. The External-2 interface handles 4 connections

## Slide 9: SD-WAN Round Robin
Example (Fireware Web UI)

## Slide 10: SD-WAN Round Robin
Optionally, you can configure loss rate, latency, and jitter measures that apply to all interfaces in the SD-WAN action
  These measures determine whether an interface qualifies to be part of the path selection
  To qualify, an interface must have loss rate, latency, and jitter values equal to or less than those you specified

## Slide 11: SD-WAN Round Robin
Add one or more policies that use the SD-WAN action
  Example HTTP and HTTPS policies

## Slide 12: SD-WAN Round Robin
The Firebox removes an interface from Round Robin path selection in these cases:
  Inactive (down) — Interface is physically disconnected, or Link Monitor probes fail
  Unqualified — Interface exceeds the loss rate, latency, or jitter values
The Firebox distributes traffic among the qualified interfaces that remain
  If no interfaces are qualified, the Firebox routes traffic to the first active (up) interface, which is the first active interface in the SD-WAN action configuration
    If no interfaces are active, the Firebox drops packets that match the SD-WAN action
    If an interface becomes active or qualified again, it automatically becomes available for Round Robin selection

## Slide 13: SD-WAN Round Robin
On the SD-WAN Status page, you can see the percent of connections handled by each interface in the SD-WAN action
  When an SD-WAN action handles many connections (hundreds or thousands), the load balancing percentage more closely matches the weight ratio
  The percentage resets after any interface status change
  For an SD-WAN action with no usage, the percentage is 0%

## Slide 14: SD-WAN Actions iN Centralized Management

## Slide 15: SD-WAN Action in Centralized Management
You can now create and apply SD-WAN actions in a Centralized Management policy template
Enables you to apply SD-WAN metrics and failback settings to multiple Fireboxes at the same time (requires the same SD-WAN action name on the Firebox)

## Slide 16: EXTERNAL VLAN Enhancements

## Slide 17: External VLAN Enhancements
To increase network design flexibility, external VLAN configurations now have fewer restrictions:
  An external VLAN can now have more than one physical interface member
  External VLAN members that are physical interfaces can now be untagged
  An interface can now simultaneously belong to both an External and Internal VLAN

## Slide 18: Set External Interface and VLAN ID in Quick Setup Wizard

## Slide 19: Set External Interface and VLAN ID in Quick Setup Wizard
You can now select which interface you want to use as the external interface in the Fireware Web UI Quick Setup Wizard
You can also enable and specify a VLAN ID for the external interface if required by your provider

## Slide 20: MOBIKE for Mobile VPN with IKEv2

## Slide 21: MOBIKE for Mobile VPN with IKEv2
Mobile VPN with IKEv2 now automatically supports the MOBIKE protocol
The Firebox can keep or reuse a VPN connection because MOBIKE allows changes to the IP address associated with IKEv2 and the tunnel mode IPSec security association (SA)
This means your remote workers can remain connected to the VPN even if they move to a different network
  For example, a remote worker is connected to Mobile VPN with IKEv2. The worker changes physical locations, which causes the laptop to connect to a different wi-fi network and obtain a different IP address. Traffic continues to flow through the tunnel, and the user does not have to re-authenticate to remain connected to the VPN.

## Slide 22: MOBIKE for Mobile VPN with IKEv2
MOBIKE applies to IKEv2 VPN clients only
  MOBIKE does not apply to the gateway
  For example, if you change the Mobile VPN with IKEv2 IP address in the Firebox configuration, users experience an interrupted VPN connection
For detailed information about the MOBIKE protocol, see RFC 4555
  In the RFC, the terms “initiator” and “responder” correspond to the IKEv2 VPN client and the Firebox, respectively

## Slide 23: INTRA-INTERFACE INSPECTION

## Slide 24: Intra-Interface Inspection
In Fireware CLI, you can now specify a command to apply firewall policies to intra-interface traffic on physical and link aggregation interfaces
  In the Configuration Command Mode, enter the Interface Command Mode and specify an interface
  To enable intra-interface inspection, run this command: intra-if-inspection enable
  To disable intra-interface inspection, run this command: no intra-if-inspection enable
Examples WG(config/if-fe01)#intra-if-inspection enable WG(config/if-fe01)#no intra-if-inspection enable

## Slide 25: Intra-Interface Inspection
To verify that intra-interface inspection is enabled or disabled, run the show interface command and specify the interface number

## Slide 26: Intra-Interface Inspection
The default intra-interface inspection behavior from previous Fireware versions remains unchanged:
  External interfaces — Enabled by default
  Non-external interfaces — Disabled by default

## Slide 27: IPv6 in Bridge Mode

## Slide 28: IPv6 in Bridge Mode
In Bridge mode, you can now specify a static IPv6 address and other IPv6 settings
On the Bridge Mode Properties page, select the IPv6 tab

## Slide 29: IPv6 in Bridge Mode
  IPv6 Bridge Mode settings
    Static IPv6 Address — Specify a system IP address and netmask for redundant management access
    (Optional) IP Address Autoconfiguration — Automatically assign an IPv6 link-local address to the interface
    (Optional) Enable DHCPv6 Client — Enable DHCPv6 clients on the interface to request an IP address from a DHCPv6 server
    (Optional) Rapid Commit — Use a two-message exchange instead of a four-message exchange for DHCPv6 requests from clients to a DHCPv6 server
    Default Gateway — Specify the gateway for the static IPv6 address (required unless you select IP Address Autoconfiguration)
    Hop Limit — Specify the number of segments a packet can traverse before a router discards it
    DAD Transmits — Specify the number of Duplication Address Detection transmits

## Slide 30: IPv6 in Bridge Mode
On the Bridge Settings tab, you can manually add IPv6 related hosts
The IPv6 gateway is added automatically to related hosts
    If you change the IPv6 gateway, the related hosts are updated automatically
Related hosts are removed if you enable IP Address Autoconfiguration or Enable DHCPv6 Client on the IPv6 tab
Related hosts must be on the same subnet as the static IPv6 address that you configured

## Slide 31: IPv6 in Bridge Mode
Related Hosts example (Fireware Web UI)

## Slide 32: IPv6 in Bridge Mode
IPv4 is always required for Bridge Mode, even if you specify IPv6 settings

## Slide 33: IPv6 in Bridge Mode
IPv6 policies
  In Bridge mode, the Firebox now supports policy matching for policies that include IPv6 hosts, IPv6 networks, and IPv6 ranges
IPv6 traffic
  If you configure a Firebox to use Bridge mode, and you do not enable IPv6, the Firebox drops IPv6 traffic that does not match a policy rather than allow the traffic to pass through the bridge
    In previous Fireware versions, which did not support IPv6 in Bridge mode, the Firebox allowed IPv6 traffic to pass through the bridge

## Slide 34: IPv6 in Bridge Mode
Bridge mode supports these Firebox features that support IPv6:
  Blocked Sites and Ports
  Quotas
  IPS and Application Control
  QoS
  Geolocation
  Traffic Management
  Schedule
  Default Packet Handling
  Proxy policies

## Slide 35: DISABLE GARP

## Slide 36: DISABLE GARP
In Mixed Routing mode only, you can now run a Fireware CLI command to disable gratuitous ARP (GARP) on Ethernet-like interfaces:
  Physical interfaces
  Link aggregation interfaces
  Bridge interfaces
  VLAN interfaces
  Wireless interfaces

## Slide 37: DISABLE GARP
By default, GARP is enabled for these interface types
  If you disable GARP, the Firebox no longer sends GARP broadcasts
You cannot disable GARP for 1-to-1 NAT or for FireCluster failover
  Even if you disable GARP for interfaces included in 1-to-1 NAT or FireCluster failover configurations, GARP broadcasts required for these features are not suppressed

## Slide 38: DISABLE GARP
To disable GARP, from Fireware CLI:
  In the Configuration Command Mode, enter the Interface Command Mode and specify an interface
  To disable GARP for the interface, run this command: no garp enable
  To enable GARP for the interface, run this command: garp enable
Examples: WG(config/if-fe01)#garp enable WG(config/if-fe01)#no garp enable

## Slide 39: DISABLE GARP
The GARP setting is added to the Firebox XML configuration and remains after a reboot

## Slide 40: Disable Geolocation Deny Page

## Slide 41: Disable the Geolocation Deny Page
In Fireware Web UI, WSM, and the Command Line Interface (CLI), you can now enable or disable the Geolocation deny page for policies
Disable the Geolocation deny page if you do not want inbound traffic to receive a deny page that attackers could use to confirm the presence of a Firebox in your network
The deny page applies to HTTP and HTTPS traffic on ports 80 and 443
In Fireware v12.8, the new Enable Deny Page check box is selected by default
To disable the deny page, clear the Enable Deny Page check box

## Slide 42: Disable Geolocation Deny Page – Web UI
To disable the deny page, from Fireware Web UI:
  Select Firewall > Firewall Policies
  Select a policy
  Select the Geolocation tab
  Clear the Enable Deny Page check box

## Slide 43: Disable Geolocation Deny Page – Policy Manager
To disable the deny page, from Policy Manager:
  Double-click a policy
  In the Edit Policy Properties dialog box, clear the Enable Deny Page check box

## Slide 44: Disable Geolocation Deny Page – CLI
To disable the deny page, from the CLI:
  Use the CLI to connect to your Firebox
  At the command prompt, type: WG(config/policy/rule-HTTP-proxy)# no geolocation deny-page enable Note: In this example, HTTP-proxy is the name of the policy

## Slide 45: Specify Logging and Notification Settings for Default Packet Handling

## Slide 46: Default Packet Handling Logging Settings
In Fireware Web UI, you can now specify logging and notification settings for different Default Packet Handling dangerous activities:
  SYN flood attack
  UDP flood attack
  ICMP flood attack
  IPsec flood attack
  IKE flood attack
  IP source route
  DDOS source attack
  DDOS destination attack
  Port scan
  IP scan
  IP spoofing attack
Select the dangerous activity and specify the log rate and notifications you want to receive when that activity is detected

## Slide 47: Default Packet Handling Logging Settings
To specify logging and notification settings by dangerous activity type, from Fireware Web UI:
  Select Firewall > Default Packet Handling
  Select the Logging tab
  Select an activity from the Select Dangerous Activity drop-down list
  Set your log and notification options for the activity

## Slide 48: APT Blocker automatically submits PDF files for Analysis

## Slide 49: APT Blocker Automatically Submits PDF Files for Analysis
APT Blocker now automatically submits unrecognized PDF files to the data center for analysis
In Fireware Web UI, on the APT Blocker page, Advanced tab, the optional check box for PDF submission is removed
In Policy Manager, for Fireboxes that run a Fireware version lower than v12.8, you can still specify whether to submit unrecognized PDF files

## Slide 50: DF Bit for Mobile VPN with IKEv2

## Slide 51: DF Bit for Mobile VPN with IKEv2
You can now specify a custom DF bit option for Mobile VPN with IKEv2 client connections
You must use this CLI command:
diagnose vpn “/ike/param/set mobile_ikev2_dfbit=(option-number)”
option-number is a number between 0 and 2 that corresponds to an option:
  0 — Copy (default). Applies the DF bit setting of the original frame to the IPSec encrypted packet
  1 — Set. Instructs the Firebox to not fragment the frame regardless of the original bit setting
  2 — Clear. Breaks the frame into pieces that can fit in an IPSec packet with the ESP or AH header, regardless of the original bit setting

## Slide 52: DF Bit for Mobile VPN with IKEv2
If you specify action=now, you do not have to restart the Firebox for this setting to take effect and the tunnel will not be rekeyed. The new timeout value that you specify will apply to new IKEv2 connections
  For example, to clear the DF bit, specify this command: WG#diagnose vpn "/ike/param/set mobile_ikev2_dfbit=2 action=now"

## Slide 53: SYSTEM Integrity Checks

## Slide 54: System Integrity Checks
The Firebox now uses a cryptographic signature to verify the integrity of the appliance
System integrity checks make sure that system files are valid and have not been corrupted
Integrity checks now run automatically:
  Each time the Firebox boots
  Before each software upgrade
You can also run an on-demand integrity check from Fireware Web UI

## Slide 55: System Integrity Checks
After you upgrade to a Fireware version that includes system integrity checks, you cannot downgrade to a Fireware version that is not signed by WatchGuard

## Slide 56: Boot Time Integrity Check
When the Firebox boots, it uses the public key installed with the appliance image to verify the integrity of the files and directories on the appliance
If the boot time integrity check fails:
  The boot process halts but power stays on
  All interfaces are disabled
  You cannot connect to the Firebox to see status
  The error Error: integrity check failed appears in the serial console

## Slide 57: Upgrade Integrity Check
The Firebox now runs an integrity check before every firmware upgrade
When you select a Fireware upgrade file to install, the Firebox makes sure the file contains a cryptographic signature
If the cryptographic signature is present, the Firebox uses the public key from the previously installed image to verify the relevant portion of the upgrade file
If the Firebox cannot verify the signature, or if the signature is not present, the Firebox refuses the upgrade

## Slide 58: On-Demand Integrity Check
You can run a Boot Time integrity check at any time from the Web UI
    Select System Status > Diagnostics (locally-managed Fireboxes) or select Diagnostics (cloud-managed Fireboxes)
    On the System Integrity tab, click Start Check
      If the on-demand integrity check fails, the Firebox generates a fault report
    To see the fault report, click the Diagnostics File tab

## Slide 59: Firebox Management Policy Warnings

## Slide 60: Firebox Management Policy Warnings
You now see a warning in the Front Panel and Policies pages (Fireware Web UI) and above the firewall policy list (Policy Manager) when your configuration includes a Firebox management policy (such as WatchGuard or WatchGuard Web UI) that allows unrestricted Internet access to your Firebox
The warning message lists any affected policies
Click the name of a policy to open and edit it

## Slide 61: Firebox Management Policy Warnings
You also see a warning message in Policy Manager and Fireware Web UI when you try to save a Firebox management policy that allows unrestricted Internet access to your Firebox
We recommend that you configure Firebox management policies to restrict management access to the Firebox
For more information, see the Firebox Remote Management Best Practices Knowledge Base article and the Secure Firebox Management Access Video Tutorial

## Slide 62: OS Checksum

## Slide 63: OS Checksum
The OS checksum feature has been deprecated and removed from Fireware Web UI and Firebox System Manager.